## Slide 1: Topological Cell Signal Clustering in the ATLAS Calorimeters (An Introduction)
Peter Loch
University of Arizona
Tucson, Arizona
USA
with a lot of input from
Sven Menke
Max Planck Institut für Physik (MPI)
Munich
Germany

## Slide 2: Roadmap
(1) Topocluster formation and noise suppression
  Clustering rules
  Cell level noise suppression
(2) Local hadronic calibration
  Topocluster classification
  Response calibration
  Signal efficiency corrections
(3) Topocluster performance in data and MC
  No/low pile-up performance (2010 data)
  Effect of high pile-up environments (2011/2012 data)
(4) Preparations for higher intensities and energies – LHC 2015 and beyond
  Conceptual issues and first performance expectations
  Extensions of calibration models and local pile-up suppression
(5) Projects for HFSF 2013 and follow-up
  Pile-up configurations and data sets
  Understanding important topocluster features in new environment – list of variables to look at, sensitivities to explore…
  Studies involving cells – infrastructure and first suggestions

## Slide 3
TopoCluster Formation and Noise Suppression

## Slide 4: Clustering Motivations & Rules (1)
Why dynamic calorimeter cell signal clustering
  Noise suppression
    Extract the (small) fraction of cells actually contributing to the collision signals – no static projection like calorimeter cell towers
  Allow local and least biased basic signal calibration
    Attempt to reconstruct a three-dimensional image of a particle shower (or overlapping showers) in the calorimeter
    Shape of reconstructed energy blob provides hint for electromagnetic or hadronic energy deposit in non-compensating calorimeter – apply corresponding calibrations cluster-by-cluster
  Reconstruct transverse momentum flow pattern
    Application in jet substructure reconstruction, event shapes, missing transverse momentum without enforcing a specific geometrical view like e.g. calorimeter cell towers
  Useful for particle ID
    E.g., tau reconstruction in ATLAS – neutral pion signal could be separated from charged pion signal with some efficiency
Notes:   Noise suppression in highly granular ATLAS calorimeters
    Only a fraction of all calorimeter cell signals are from physics objects – exact quantity depends on final state
    Adding cells without “true” signal in physics object reconstruction increases signal fluctuations for the reconstructed object and thus reduces resolution
    Need (mostly) signal definition with high efficiency for true signal to survive while irrelevant signals to be suppressed
  Local signal scales in non-compensating calorimeters
    Classical approach (e.g. Tevatron) – apply all calibrations and corrections to fully reconstructed objects like particles and jets – leads to large corrections and scales to be applied
    Inter-calibration between signals from various calorimeter regions, particle types and particle energies can be typically wrong up to 60% or more – can be a problem for internal pT scales in recursive recombination jet algorithms, jet substructure, and global event quantities like missing transverse energy and event shapes (mostly with respect to resolution and signal stability)
    Can be addressed by local calibration not biased with respect to a given physics object type

## Slide 5: Clustering Motivations & Rules (2)
Guidelines for clustering algorithm
  Follow significant and connected signal patterns in the calorimeter cells
    Ideally trace the correlations between cell signals introduced by individual or overlapping electromagnetic and/or hadronic showers in an attempt to reconstruct isolated and merged particle cascades
    Basic scale for measuring significance in each cell is its noise – underlying signal fluctuations introduced by elementary readout and signal processing, and the pile-up signal history.
    Connect cells in three dimensions to form localized “energy blobs” in the calorimeter (topological nearest-neighbor clustering)
  Let cell signal and its environment define cell contribution
    Small signals in close proximity to large signals are likely from true energy deposits – even if the (isolated) signal significance is low
    Large signals – seeds, smaller signals – control growth around seeds
  Control cluster growth
    Important (transverse) momentum flow patterns relevant for any final state should be preserved with high sensitivity

## Slide 6: Topological Cell Cluster Implementation
Collect cell into energy “blobs”
  Idea is to collect all cell signals belonging to a given particle into one cluster of cells
    Basically reconstruct the shower for each particle entering the calorimeter
  Needs algorithm to form energy blobs at the location of the shower signal in the calorimeter
    Follow the shower-induced cell signal correlations
Extract most significant signal from all calorimeter cells
  Cluster formation uses signal significance as guidance
    Not the total signal – noise changes from calorimeter region to calorimeter region
  Implicit noise suppression in cluster formation
    Cluster signals should include least amount of noise

## Slide 7: Topological Cell Cluster Implementation
Collect cell into energy “blobs”
  Idea is to collect all cell signals belonging to a given particle into one cluster of cells
    Basically reconstruct the shower for each particle entering the calorimeter
  Needs algorithm to form energy blobs at the location of the shower signal in the calorimeter
    Follow the shower-induced cell signal correlations
Extract most significant signal from all calorimeter cells
  Cluster formation uses signal significance as guidance
    Not the total signal – noise changes from calorimeter region to calorimeter region
  Implicit noise suppression in cluster formation
    Cluster signals should include least amount of noise
Electronic Noise in Calorimeter Cells
S. Menke, ATLAS Physics Workshop 07/2005
Pile-up Noise in Calorimeter Cells
S. Menke, ATLAS Physics Workshop 07/2005

## Slide 8: ATLAS Topological Cell Clustering
Cluster seeding
  Defined by signal significance above primary threshold
    Cells above this threshold can seed cluster
Cluster growth
  Defined by signal significance above secondary threshold
    Cells neighbouring seeds with significance above this threshold drive cluster growths
Cluster signal
  Defined by cells with significance above basic threshold
    Cells to be considered in cluster energy sums
Use of negative signal cells
  Thresholds are considered for the absolute (unsigned) signal magnitude
    Large negative signals can seed and grow clusters
Parameters for each stage optimized with testbeam data
  Experimental single pion shower shapes guide cluster algorithm develpoment
    Clean tuning reference!
Famous “4/2/0” clustering in ATLAS

## Slide 9: ATLAS Topological Cell Clustering
Cluster seeding
  Defined by signal significance above primary threshold
    Cells above this threshold can seed cluster
Cluster growth control
  Defined by signal significance above secondary threshold
    Cells neighbouring seeds with significance above this threshold drive cluster growths
Cluster signal
  Defined by cells with significance above basic threshold
    Cells to be considered in cluster energy sums
Use of negative signal cells
  Thresholds are considered for the absolute (unsigned) signal magnitude
    Large negative signals can seed and grow clusters
Parameters for each stage optimized with testbeam data
  Experimental single pion shower shapes guide cluster algorithm develpoment
    Clean tuning reference!
 P
 N
 S
180 GeV pions
Resolution of Sum Eclus
 S
 N
 P
Mean of Sum Eclus

## Slide 10: Clustering Algorithms
Find cell with most significant seed over primary threshold S
Collect all cells with significance above basic threshold P
  Consider neighbours in three dimensions
    Defined by (partly) shared area, (partly) shared edge, or shared corner point
    E.g., 26 neighbours for perfectly cubed volumes of equal size
  Neighbours can be in other calorimeter regions or even other calorimeter sub-systems
    Granularity change to be considered in neighbouring definition
For all cells neighbouring seeds with signal significance above secondary threshold N, collect neighbours of neighbours if their signal significance is above P
  Same rules as for collection around primary seed
Continue until cluster does not grow anymore
  Automatically generate “guard ring” of small signal cells at cluster margin
    In three dimensions, of course
Take next not yet used seed cell and collect next cluster

## Slide 11: Clustering

## Slide 12: Clustering Example

## Slide 13: Clustering Example

## Slide 14: Clustering Example

## Slide 15: Clustering Example

## Slide 16: Clustering Example

## Slide 17: Clustering Example

## Slide 18: Clustering Example

## Slide 19: Clustering Example

## Slide 20: Clustering Example

## Slide 21: Clustering Example

## Slide 22: Clustering Example

## Slide 23: Clustering Example

## Slide 24: Clustering Example

## Slide 25: Clustering Example

## Slide 26: Clustering Example

## Slide 27: Clustering Example

## Slide 28: Clustering Example

## Slide 29: Clustering Example

## Slide 30: Clustering Example

## Slide 31: Clustering Example

## Slide 32: Clustering Example

## Slide 33: Clustering Example

## Slide 34: Clustering Example

## Slide 35: Clustering Example

## Slide 36: Clustering Example

## Slide 37: Effect Of Strict Nearest Neighbour Approach
Large topologically connected regions in calorimeter can lead to large cell clusters
  Lost particle flow structure can introduce problems for jets
    Infrared safety, in particular
  Need to refine the clustering algorithm
    Try to match single particle shower shapes better
Splitting the clusters
  Examine spatial cluster signal structure – find local signal maxima
    “hill and valley” structural analysis in three dimensions
  Split cluster between two maxima
    In three dimensions, of course!
  Share energy of cells in signal valleys
    Needs sharing rules – introduces “geometrically” weighted cell energy contribution to cluster signal
  Introduces new tunable parameter
    Local signal maximum threshold is defined in units of energy, not significance!

## Slide 38: Cluster Splitting

## Slide 39: Cluster Splitting

## Slide 40: Cluster Splitting

## Slide 41: Splitting & Cell Energy Sharing
Splitting technique
  Guided by finest calorimeter granularity
    Typically in electromagnetic calorimeter
  Allows to split larger cell signals without signal valley
    Typically in hadronic calorimeters

## Slide 42: Splitting & Cell Energy Sharing
Splitting technique
  Guided by finest calorimeter granularity
    Typically in electromagnetic calorimeter
  Allows to split larger cell signals without signal valley
    Typically in hadronic calorimeters

## Slide 43: Single Particle Clusters

## Slide 44: Cluster Shapes
Clusters have shapes
  Geometrical moments and sizes
    Lateral and longitudinal
  Tilt of principal axis
    With respect to direction extrapolation from primary vertex (magnetic field!)
  Density and compactness measures
    Cluster energy distribution in cells
  Energy sharing between calorimeter segments and modules
    Shower structures
Useful for cluster calibration
  Exploit shape sensitivity to shower character
    Hadronic versus electromagnetic

## Slide 45: Cell Signal Significance In Clusters (1)

## Slide 46: Cell Signal Significance In Clusters (2)
For this week:
  Fraction of cells surviving clustering
    5-20% for example data set, dependent on calorimeter region
  Partial Gauss fits
    Measure mop and sigma before (expected <0) and after (expected >0) clustering

## Slide 47: Cluster Kinematics
Cluster signal
  Sum of clustered cell energies
    Possibly with geometrical weight introduced by cluster splitting
Cluster direction & location
  Barycenter in (η,φ) from energy weighted cell directions
    Negative signal cells contribute with absolute of their signal
    Small effect on direction of final cluster from particles – negative signals are noise, i.e. small!
  Consistent approach for direction calculation
    Leaves true signal and noise clusters at the right direction
  Same approach for geometrical signal center
    “center of gravity”
Cluster four-momentum
  Massless pseudo-particle approach similar to tower
    Consistent with cluster idea of reconstructing showers rather than particles

## Slide 48: Cluster Kinematics
Cluster signal
  Sum of clustered cell energies
    Possibly with geometrical weight introduced by cluster splitting
Cluster direction & location
  Barycenter in (η,φ) from energy weighted cell directions
    Negative signal cells contribute with absolute of their signal
    Small effect on direction of final cluster from particles – negative signals are noise, i.e. small!
  Consistent approach for direction calculation
    Leaves true signal and noise clusters at the right direction
  Same approach for geometrical signal center
    “center of gravity”
Cluster four-momentum
  Massless pseudo-particle approach similar to tower
    Consistent with cluster idea of reconstructing showers rather than particles

## Slide 49: Cluster Features
Signal integration
  Clusters sum cell signals without grid
    3-dimensional signal objects
    Can include partial and complete signals from several particles
  Clusters preserve some detailed signal features
    Associated information to be collected at cluster formation
    E.g., energy sharing in electromagnetic and hadronic calorimeters
    Longitudinal signal center of gravity
    Shapes
Signal splitting
  Topological clusters need splitting algorithm
    Cannot follow individual showers perfectly in jet environments
    Can cause problems with infrared safety
  Few problems with seed and energy leakage
    Can include energy from cells even outside of jet cone
Topological cell cluster is a “blob” of energy dynamically located inside the calorimeter (even crossing sub-detector boundaries)
(drawing by R. Walker, University of Arizona)

## Slide 50
Local Hadronic Calibration

## Slide 51: Cluster Calibration
General cluster features
  Motivated by shower reconstruction
    No bias in signal definition towards reconstruction of a certain, possibly very specific, physics signal object like a jet
  Clusters have shapes and location information
    Spatial cell energy distributions and their correlations drive longitudinal and lateral extensions
    Density and energy sharing measures
    Signal center of gravity and (directional) bary-center
  Shapes are sensitive to shower nature
    At least for a reasonable clustering algorithm
Local (cluster) calibration strategy
  First reconstruct truly deposited energy at cluster location…
    e/h, mostly
  …then correct for other energy losses in the vicinity of signal cluster
    Dead material energy losses and signal losses due to noise suppression
Calibration input
  Reconstructed cluster shapes represent shower shapes
    E.g., dense and compact clusters indicate electromagnetic shower activity anywhere in the calorimeter
      Can be intrinsic to a hadronic shower!
    Calibration functions can exploit the cluster shapes to apply the corrections for e/h ≠ 1 dynamically
  Location of cluster together with shape
    E.g., dense and compact clusters located in electromagnetic calorimeter indicate electron or photon as particle originating the signal
      Cluster not (part of) hadronic shower signal!
    Clusters can classified before calibration
      Electron/photon clusters need different calibration than dense clusters from hadronic showers!
Cluster calibration extensions
  Shapes, location and size also indicate possible energy losses around the cluster
    Some correlations between energy losses in inactive material in front or inside of clusters
  Cluster size and signal neighborhood sensitive to lost true signal in noise suppression algorithm
    Out-of-cluster corrections

## Slide 52: Cluster Calibration Sequence

## Slide 53: Hadronic Cluster Calibration
Calibration with cell signal weights
  Idea is to compensate for lack of pion response in each cell
    Pioneered in CDHS and applied in H1

## Slide 54: Hadronic Cluster Calibration
Calibration with cell signal weights
  Idea is to compensate for lack of pion response in each cell
    Pioneered in CDHS and applied in H1

## Slide 55: Hadronic Cluster Calibration
Calibration with cell signal weights
  Idea is to compensate for lack of pion response in each cell
    Pioneered in CDHS and applied in H1

## Slide 56: Hadronic Cluster Calibration
Calibration with cell signal weights
  Idea is to compensate for lack of pion response in each cell
    Pioneered in CDHS and applied in H1

## Slide 57: Hadronic Cluster Calibration
Calibration with cell signal weights
  Idea is to compensate for lack of pion response in each cell
    Pioneered in CDHS and applied in H1
  Uses deposited energies in cells
    Deposit can be in active or passive medium of calorimeter!

## Slide 58: Hadronic Cluster Calibration
Calibration with cell signal weights
  Idea is to compensate for lack of pion response in each cell
    Pioneered in CDHS and applied in H1
  Uses deposited energies in cells
    Deposit can be in active or passive medium of calorimeter!
Only signal contribution from energy deposited by electromagnetic sub-showers and through ionization by charged particles!

## Slide 59: Hadronic Cluster Calibration
Calibration with cell signal weights
  Idea is to compensate for lack of pion response in each cell
    Pioneered in CDHS and applied in H1
  Uses deposited energies in cells
    Deposit can be in active or passive medium of calorimeter!
Energy deposited in cell not available in experiment
  Use of detector simulations
    Deposited energy and signal available
    Use “unit cell” volume concept to collect invisible energies
    Shower model dependent!
  Use single pion testbeam data
    Develop model for weights in cells
    Fit parameters of model using cells testbeam
      Minimize resolution with beam energy constraint
    Statistical – does not necessarily produce the correct weights!

## Slide 60: Cell Signal Weights
Basic idea
  Use a dynamically self-adjusting calibration weight
    High cell signal density → electromagnetic deposit
    Low cell signal density → hadronic deposit
  Principal weighting function characteristics
    Depends on cell energy density
    Depends on cell location
    Accidental application to electron signals should yield correct energy as well
Extraction of weighting functions
  Minimize resolution in (pion) testbeam data
    Fitting function model
    May not produce the correct weights – may even be unphysical!
  Use simulation
    Deterministic approach relates signal to deposited energy within cell volume – no fitting!
    May depend on details of (hadronic) shower modeling
ATLAS cluster-based approach:
Use only cells in hadronic clusters
Cluster sets global energy scale as a reference for densities
Calculate Edeposited,cell/E0,cell from single pion simulations in bins of cluster energy, cell energy density, cluster direction, and calorimeter sampling layer
Store [Edeposited,cell/E0,cell]-1 in look-up tables
Retrieve weights for any cell in any cluster from look-up table to reconstruct cell and cluster energies

## Slide 61: Cell Signal Weights
Basic idea
  Use a dynamically self-adjusting calibration weight
    High cell signal density → electromagnetic deposit
    Low cell signal density → hadronic deposit
  Principal weighting function characteristics
    Depends on cell energy density
    Depends on cell location
    Accidental application to electron signals should yield correct energy as well
Extraction of weighting functions
  Minimize resolution in (pion) testbeam data
    Fitting function model
    May not produce the correct weights – may even be unphysical!
  Use simulation
    Deterministic approach relates signal to deposited energy within cell volume – no fitting!
    May depend on details of (hadronic) shower modeling
ATLAS cluster-based approach:
Use only cells in hadronic clusters
Cluster sets global energy scale as a reference for densities
Calculate Edeposited,cell/E0,cell from single pion simulations in bins of cluster energy, cell energy density, cluster direction, and calorimeter sampling layer
Store [Edeposited,cell/E0,cell]-1 in look-up tables
Retrieve weights for any cell in any cluster from look-up table to reconstruct cell and cluster energies

## Slide 62: Cell Signal Weights
Basic idea
  Use a dynamically self-adjusting calibration weight
    High cell signal density → electromagnetic deposit
    Low cell signal density → hadronic deposit
  Principal weighting function characteristics
    Depends on cell energy density
    Depends on cell location
    Accidental application to electron signals should yield correct energy as well
Extraction of weighting functions
  Minimize resolution in (pion) testbeam data
    Fitting function model
    May not produce the correct weights – may even be unphysical!
  Use simulation
    Deterministic approach relates signal to deposited energy within cell volume – no fitting!
    May depend on details of (hadronic) shower modeling
ATLAS cluster-based approach:
Use only cells in hadronic clusters
Cluster sets global energy scale as a reference for densities
Calculate Edeposited,cell/E0,cell from single pion simulations in bins of cluster energy, cell energy density, cluster direction, and calorimeter sampling layer
Store [Edeposited,cell/E0,cell]-1 in look-up tables
Retrieve weights for any cell in any cluster from look-up table to reconstruct cell and cluster energies
Note that re-calculation of cluster kinematics (energy and directions) using calibrated (weighted) cell signals changes not only the cluster energy, but also the cluster direction (bary-center) and its geometrical center!

## Slide 68: Cluster Dead Material Corrections
Dead material
  Energy losses not directly measurable
    Signal distribution in vicinity can help
  Introduces need for signal corrections up to O(10%)
    Exclusive use of signal features
    Corrections depend on electromagnetic or hadronic energy deposit
  Major contributions
    Upstream materials
    Material between LArG and Tile (central)
Cracks
  dominant sources for signal losses
    |η|≈1.4-1.5
    |η|≈3.2
  Clearly affects detection efficiency for particles and jets
    Already in trigger!
    Hard to recover jet reconstruction inefficiencies
  Generate fake missing Et contribution
    Topology dependence of missing Et reconstruction quality
Additive correction:
Relative energy loss in dead material
Relative energy loss in dead material

## Slide 69: Out-of-cluster Corrections
Compensate loss of true signal
  Limited efficiency of noise suppression scheme
    Discard cells with small true energy not close to a primary or secondary seed
    Accidental acceptance of a pure noise cell
  Can be significant for isolated pions
    10% at low energy
  Correction derived from single pions
    Compensates the isolated particle loss
    But in jets neighboring clusters can pick up lost energy
  Use isolation moment to measure effective “free surface” of each cluster
    Scale single pion correction with this moment (0…1)
Additive correction:
single pions
QCD jets

## Slide 70
TopoCluster Performance
In Data & MC

## Slide 71: Validation of TopoCluster Moments
(all plots on this slide from ATLAS-CONF-2010-053)
cluster depth (EM)
cluster depth (HAD)
cluster
isolation
(EM)
cluster
isolation
(HAD)
  Complex cluster observables well described in MC
    Distributions affected by shower structures, detector geometries, noise patterns, …
    Simulation works well inside and outside of jets
Local Hadronic Calibration (LCW) in cluster context
  Attempt to reduce signal fluctuations dynamically
    Explicit use of calorimeter signal features, e.g. cell energy density, spatial cell signal distribution
  Applied at topological cell cluster level
    Exploits cluster kinematics, shapes & location
2010 Data/MC

## Slide 72: Cluster Variable Validation
Mean isolation for EM & HAD clusters
Average cluster depth
EM clusters
HAD clusters
EM clusters
HAD clusters
2010 Data/MC

## Slide 73: Jet Input Validation – Local Hadronic Energy Scale
LCW – cluster context hadronic calibration
  Highly factorized scheme
    Implements cluster classification specific calibration chains for electromagnetic and hadronic clusters
    Corrections derived independently using detailed single particle simulations
    All corrections derived from deposited energies at or around cluster location and their relation to the signal features
  High demand on (detector) simulation quality
    Each step validated with collision data
  Calibration signal calibrations & corrections well reproduced even for clusters inside jets
    Non-trivial confirmation of approach due to complex variable space and single particle source for parameters and functions
    No significant quality variations as function of cluster location or transverse momentum
(all plots from ATLAS-CONF-2010-053)
hadronic response
+ out of cluster
+ dead material
2010 Data/MC

## Slide 74: Jet Input Validation – Local Hadronic Energy Scale
LCW – cluster context hadronic calibration
  Highly factorized scheme
    Implements cluster classification specific calibration chains for electromagnetic and hadronic clusters
    Corrections derived independently using detailed single particle simulations
    All corrections derived from deposited energies at or around cluster location and their relation to the signal features
  High demand on (detector) simulation quality
    Each step validated with collision data
  Calibration signal calibrations & corrections well reproduced even for clusters inside jets
    Non-trivial confirmation of approach due to complex variable space and single particle source for parameters and functions
    No significant quality variations as function of cluster location or transverse momentum
(all plots from ATLAS-CONF-2010-053)
hadronic response
+ out of cluster
+ dead material
hadronic response
+ out of cluster
+ dead material
2010 Data/MC

## Slide 75
2011 MC

## Slide 76
2011 MC

## Slide 77
2011 MC

## Slide 78
2011 MC

## Slide 79: High Pile-up 2012
No dedicated study of 2011/2012 cluster properties in data (yet?)
  Revival in the context of the TopoCluster paper – the hope!
    We are trying to get this together Spring 2014…
  See material attached to agenda for more information about clusters in pile-up…

## Slide 80
Preparations for Higher Intensities and Energies
LHC 2015 & Beyond…

## Slide 81: Future of TopoClusters (MHO!)
Formation
  No particular need to change cluster formation
    More important: update pilep-up fluctuations (RMS) – uses very old MC estimates, likely very wrong for endcap/forward
    More plots to confirm this week!
  Splitting scale is looked at
    Plays ~0 role in cluster splitting in 2012 anyway, due to higher reconstruction thresholds – not a very critical parameter
    Different (separate) treatment of (groups of) negative cells – not clear if this is useful? We can look at the HCW2013 contribution if interested…

## Slide 82: Future of TopoClusters (MHO!)
Local calibration
  Hadronic cell weights from single particle signals at chosen sigma
    Important choice – works best if sigma matches fluctuations at the “same” μ!
    Note that signals and truth reference do not include pile-up (in-time or out-of-time!
  Task: check phase space for parameters used in calibrations and corrections in the presence of pile-up
    Cluster shape/density/location modifications possibly shifting parameters and correlations outside of phase space covered by single pion MC…

## Slide 83: Future of TopoClusters (MHO)
Pile-up suppression of clusters
  Based on track-cluster matching
    Potential to remove clusters matched to a non-primary vertex track…
  Some concerns
    Imbalance of neutral and charged response inside and outside e.g. jets
    Stability of “classification” – easier to see for jets with finite catchment area, cluster catchment area not so clear…

## Slide 84
Backup [1]
Principles of Calorimetry

## Slide 85: Principles of Calorimetry
Detector needs for multi-purpose collider experiments
  Tracking for charged particle momentum measurement
  Calorimeters for charged and neutral particle energy measurement
  Muon spectrometers (tracking) for muon momentum measurements
Underlying physics for calorimetry: particle interaction with matter
  Electromagnetic cascades
  Hadronic cascades
  Muon energy loss
Calorimetric principles in particle detection
  Conversion of deposited energy into an extractable signal in homogeneous and sampling calorimeters
  Minimum ionizing particles and muons
  General signal features of electromagnetic and hadronic showers
Calorimeter characteristics in sampling calorimeters
  Sampling fraction
  Signal linearity and relative resolution
  Non-compensation
Signal extraction
  Charge collection
  Current measurement
  Pulse shapes

## Slide 86: Particle Interaction with Matter
Cascades or showers
  Most particles entering matter start a shower of secondary particles
    Exception: muons and neutrinos
  The character of these cascades depends on the nature of the particle
    Electrons, photons: cascades are formed by QED processes
    Hadrons: cascades are dominantly formed by QCD processes
  Extensions/size of these showers
    Again depends on particle type
    Electromagnetic showers typically small and compact
    Hadronic showers much larger
    Common feature: shower depths scales approximately as log(E)
      Higher energies do not require much deeper detectors!
      But very different longitudinal and radial scales - material and particle type dependent!
Shower development and age
  Shower maximum
    Depth at which average energy of shower particles is too small to continue production of secondaries – shower development starts to slow down/stop
  Age of shower
    Depth of shower
  Shower width
    Extend of shower perpendicular to direction of flight of incoming particle

## Slide 87: Electromagnetic Showers
QED drives cascade development
  High energetic electrons entering material emit photons in the electric field of the nuclei
    Bremsstrahlung
  High energetic photons produce e+e- pairs in the electric field of the nuclei
    Pair production
Rossi’s shower model (1952!)
  Simple model of interplay of electron energy loss and photon pair production
    Uses critical energy as cutoff for shower development

## Slide 88: Electromagnetic Showers
QED drives cascade development
  High energetic electrons entering material emit photons in the electric field of the nuclei
    Bremsstrahlung
  High energetic photons produce e+e- pairs in the electric field of the nuclei
    Pair production
Rossi’s shower model (1952!)
  Simple model of interplay of electron energy loss and photon pair production
    Uses critical energy as cutoff for shower development

## Slide 89: Electromagnetic Showers
QED drives cascade development
  High energetic electrons entering material emit photons in the electric field of the nuclei
    Bremsstrahlung
  High energetic photons produce e+e- pairs in the electric field of the nuclei
    Pair production
Rossi’s shower model (1952!)
  Simple model of interplay of electron energy loss and photon pair production
    Uses critical energy as cutoff for shower development

## Slide 90: Electromagnetic Showers
QED drives cascade development
  High energetic electrons entering material emit photons in the electric field of the nuclei
    Bremsstrahlung
  High energetic photons produce e+e- pairs in the electric field of the nuclei
    Pair production
Rossi’s shower model (1952!)
  Simple model of interplay of electron energy loss and photon pair production
    Uses critical energy as cutoff for shower development

## Slide 91: Electromagnetic Showers
QED drives cascade development
  High energetic electrons entering material emit photons in the electric field of the nuclei
    Bremsstrahlung
  High energetic photons produce e+e- pairs in the electric field of the nuclei
    Pair production
Rossi’s shower model (1952!)
  Simple model of interplay of electron energy loss and photon pair production
    Uses critical energy as cutoff for shower development

## Slide 92: Hadronic Showers
QCD drives fast shower development
  Hadron interacts with nucleon in nuclei
    Like a fixed target collision
    Develops intra-nuclear cascade (fast)
  Hadron production
    Secondary hadrons escape nucleus
    Neutral pions decay immediately into 2 photons → electromagnetic cascade
    Other hadrons can hit other nucleons → inter-nuclear cascade
Slow de-excitation of nuclei
  Remaining nucleus in excited state
    Evaporates energy to reach stable (ground) state
    Fission and spallation possible
  Binding energy and low energetic photons
Large process fluctuations
  ~200 different interactions
  Probability for any one of those < 1%!

## Slide 93: Hadronic Showers
QCD drives fast shower development
  Hadron interacts with nucleon in nuclei
    Like a fixed target collision
    Develops intra-nuclear cascade (fast)
  Hadron production
    Secondary hadrons escape nucleus
    Neutral pions decay immediately into 2 photons → electromagnetic cascade
    Other hadrons can hit other nucleons → inter-nuclear cascade
Slow de-excitation of nuclei
  Remaining nucleus in excited state
    Evaporates energy to reach stable (ground) state
    Fission and spallation possible
  Binding energy and low energetic photons
Large process fluctuations
  ~200 different interactions
  Probability for any one of those < 1%!

## Slide 94: Hadronic Showers
QCD drives fast shower development
  Hadron interacts with nucleon in nuclei
    Like a fixed target collision
    Develops intra-nuclear cascade (fast)
  Hadron production
    Secondary hadrons escape nucleus
    Neutral pions decay immediately into 2 photons → electromagnetic cascade
    Other hadrons can hit other nucleons → internuclear cascade
Slow de-excitation of nuclei
  Remaining nucleus in excited state
    Evaporates energy to reach stable (ground) state
    Fission and spallation possible
  Binding energy and low energetic photons
Large process fluctuations
  ~200 different interactions
  Probability for any one of those < 1%!
Grupen,
Particle Detectors
Cambridge University Press (1996)

## Slide 95: Hadronic Showers
GEANT4 Simulation: 10 GeV π+ in copper

## Slide 96: Calorimeter Basics (1)
Full absorption detector
  Idea is to convert incoming particle energy into detectable signals
    Light or electric current
    Should work for charged and neutral particles
  Exploits the fact that particles entering matter deposit their energy in particle cascades
    Electrons/photons in electromagnetic showers
    Charged pions, protons, neutrons in hadronic showers
    Muons do not shower at all in general
Principal design challenges
  Need dense matter to absorb particles within a small detector volume
    Lead for electrons and photons, copper or iron for hadrons
  Need “light” material to collect signals with least losses
    Scintillator plastic, nobel gases and liquids
  Solution I: combination of both features
    Crystal calorimetry, BGO
  Solution II: sampling calorimetry

## Slide 97: Calorimeter Basics (2)
Sampling calorimeters
  Use dense material for absorption power…
    No direct signal
  …in combination with highly efficient active material
    Generates signal
  Consequence: only a certain fraction of the incoming energy is directly converted into a signal
    Typically 1-10%
  Signal is therefore subjected to sampling statistics
    The same energy loss by a given particle type may generate different signals
    Limit of precision in measurements
Need to understand particle response
  Electromagnetic and hadronic showers

## Slide 98: Electromagnetic Cascades in Calorimeters
Electromagnetic showers
  Particle cascade generated by electrons/positrons and photons in matter
  Developed by bremsstrahlung & pair-production
Compact signal expected
  Regular shower shapes
    Small shower-to-shower fluctuations
  Strong correlation between longitudinal and lateral shower spread
RD3 note 41, 28 Jan 1993
C. Amsler et al. (Particle Data Group), Physics Letters B667, 1 (2008) and 2009 partial update for the 2010 edition

## Slide 99: Electromagnetic Cascades in Calorimeters
Electromagnetic showers
  Particle cascade generated by electrons/positrons and photons in matter
  Developed by bremsstrahlung & pair-production
Compact signal expected
  Regular shower shapes
    Small shower-to-shower fluctuations
  Strong correlation between longitudinal and lateral shower spread
RD3 note 41, 28 Jan 1993
C. Amsler et al. (Particle Data Group), Physics Letters B667, 1 (2008) and 2009 partial update for the 2010 edition

## Slide 100: Electromagnetic Cascades in Calorimeters
Electromagnetic showers
  Particle cascade generated by electrons/positrons and photons in matter
  Developed by bremsstrahlung & pair-production
Compact signal expected
  Regular shower shapes
    Small shower-to-shower fluctuations
  Strong correlation between longitudinal and lateral shower spread
RD3 note 41, 28 Jan 1993
P. Loch (Diss.), University of Hamburg 1992

## Slide 101: Electromagnetic Cascades in Calorimeters
Electromagnetic showers
  Particle cascade generated by electrons/positrons and photons in matter
  Developed by bremsstrahlung & pair-production
Compact signal expected
  Regular shower shapes
    Small shower-to-shower fluctuations
  Strong correlation between longitudinal and lateral shower spread
RD3 note 41, 28 Jan 1993
G.A. Akopdzhanov et al. (Particle Data Group), Physics Letters B667, 1 (2008) and 2009 partial update for the 2010 edition
P. Loch (Diss.), University of Hamburg 1992

## Slide 102: Hadronic Cascades in Calorimeters
Hadronic signals
  Much larger showers
    Need deeper development
    Wider shower spread
  Large energy losses without signal generation in hadronic shower component
    Binding energy losses
    Escaping energy/slow particles (neutrinos/neutrons)
  Signal depends on size of electromagnetic component
    Energy invested in neutral pions lost for further hadronic shower development
    Fluctuating significantly shower-by-shower
    Weakly depending on incoming hadron energy
Consequence: non-compensation
  Hadrons generate less signal than electrons depositing the same energy
5 GeV electrons
30 GeV pions
P. Loch (Diss.), University of Hamburg 1992
30 GeV electrons

## Slide 103: Hadronic Cascades in Calorimeters
Hadronic signals
  Much larger showers
    Need deeper development
    Wider shower spread
  Large energy losses without signal generation in hadronic shower component
    Binding energy losses
    Escaping energy/slow particles (neutrinos/neutrons)
  Signal depends on size of electromagnetic component
    Energy invested in neutral pions lost for further hadronic shower development
    Fluctuating significantly shower-by-shower
    Weakly depending on incoming hadron energy
Consequence: non-compensation
  Hadrons generate less signal than electrons depositing the same energy
P. Loch (Diss.), University of Hamburg 1992
30 GeV π ̶
80 GeV π ̶
5 GeV π ̶

## Slide 104: Shower Features Summary
Electromagnetic
  Compact
    Growths in depth ~log(E)
  Longitudinal extension scale is radiation length X0
    Distance in matter in which ~50% of electron energy is radiated off
    Photons 9/7 X0
  Strong correlation between lateral and longitudinal shower development
  Small shower-to-shower fluctuations
    Very regular development
  Can be simulated with high precision
    1% or better, depending on features
Hadronic
  Scattered, significantly bigger
    Growths in depth ~log(E)
  Longitudinal extension scale is interaction length λ >> X0
    Average distance between two inelastic interactions in matter
    Varies significantly for pions, protons, neutrons
  Weak correlation between longitudinal and lateral shower development
  Large shower-to-shower fluctuations
    Very irregular development
  Can be simulated with reasonable precision
    ~2-5% depending on feature

## Slide 105
Backup [2]
Calorimeter Signal
Formation

## Slide 106: Signal Formation: Electromagnetic Signals
Signal features in sampling calorimeters
  Collected from ionizations in active material
    Not all energy deposit converted to signal
  Proportional to incoming electron/photon
    C.f. Rossi’s shower model, Approximation B
      Only charged tracks contribute to signal
      Only pair-production for photons
      Energy loss is constant
    Signal proportional to integrated shower particle path
  Stochastical fluctuations
    Sampling character
  Sampling fraction
    Describes average fraction of deposited energy generating the signal

## Slide 107: Signal Formation: Sampling Fraction
Characterizes sampling calorimeters
  Ratio of energy deposited in active material and total energy deposit
  Assumes constant energy loss per unit depth in material
    Ionization only
  Can be adjusted when designing the calorimeter
    Material choices
    Readout geometry
Multiple scattering
  Changes sampling fraction
    Effective extension of particle path in matter
    Different for absorber and active material
Showering
  Cannot be included in sampling fraction analytically
    Need measurements and/or simulations

## Slide 108: Signal Formation: Sampling Fraction
Characterizes sampling calorimeters
  Ratio of energy deposited in active material and total energy deposit
  Assumes constant energy loss per unit depth in material
    Ionization only
  Can be adjusted when designing the calorimeter
    Material choices
    Readout geometry
Multiple scattering
  Changes sampling fraction
    Effective extension of particle path in matter
    Different for absorber and active material
Showering
  Cannot be included in sampling fraction analytically
    Need measurements and/or simulations
C. Amsler et al. (Particle Data Group), Physics Letters B667, 1 (2008) and 2009 partial update for the 2010 edition

## Slide 109: Signal Formation: Sampling Fraction
Characterizes sampling calorimeters
  Ratio of energy deposited in active material and total energy deposit
  Assumes constant energy loss per unit depth in material
    Ionization only
  Can be adjusted when designing the calorimeter
    Material choices
    Readout geometry
Multiple scattering
  Changes sampling fraction
    Effective extension of particle path in matter
    Different for absorber and active material
Showering
  Cannot be included in sampling fraction analytically
    Need measurements and/or simulations
Showering changes the electron sampling fraction mostly due to the strong dependence of photon capture (photo-effect) on the material (cross-section ~Z5) leading to a non-proportional absorption of energy carried by soft photons deeper in the shower!
P. Loch (Diss.), University of Hamburg 1992
5 GeV
30 GeV
80 GeV
Electrons

## Slide 110: Signal Extraction
Example: charge collection in noble liquids
  Charged particles ionizing active medium when traversing it
    Fast passage compared to electron drift velocity in medium
  Electrons from these ionizations are collected in external electric field
    Similar to collection of 1-dim “line of charges” with constant charge density
  Resulting (electron) current is base of signal
    Positive ions much slower
    Can collect charges or measure current
Characteristic features
  Collected charge and current are proportional to energy deposited in active medium
  Drift time for electrons in active medium
    Determines charge collection time
    Can be adjusted to optimize calorimeter performance

## Slide 111
Backup [3]
Signals in the ATLAS LAr Calorimeters

## Slide 112: ATLAS Calorimeter Signal Extraction
What is response?
  Reconstructed calorimeter signal
    Based on the direct measurement – the raw signal
    May include noise suppression
  Has the concept of signal (or energy) scale
    Mostly understood as the basic signal before final calibrations
  Does not explicitly include particle or jet hypothesis
    Uses only calorimeter signal amplitudes, spatial distributions, etc.

## Slide 113: Calorimeter Signal in ATLAS
Slow signal collection in liquid argon calorimeters
  ~450 ns @ 1 kV/mm drift time versus 40 MHz/25 ns bunch crossing time
    Measure only I0 = I(t0) (integrate <25 ns)
  Applying a fast bi-polar signal shaping
    Shaping time ~15 ns
      With well known shape
    Shaped pulse integral = 0
      Net average signal contribution from pile-up = 0
      Need to measure the pulse shape (time sampled readout)
    Total integration ~25 bunch crossings
      23 before signal, 1 signal, 1 after signal
reading out (digitize) 5 samples sufficient!

## Slide 114: Pile-up Suppression in ATLAS
General strategies
  Build calorimeter with relatively fast signal collection
    E.g., ATLAS tile, CMS crystal & tile
    Only sensitive to small time window around triggered signal
  Convert slow pulse to net-zero area bi-polar pulse
    E.g, ATLAS liquid argon
    Measures initial current rather than total charge
    Signals from pile-up history suppress in-time pile-up contribution due to pulse shape
  Exercise
    Pile-up suppression in various LHC bunch crossing timing
past bunch crossings
following bunch crossings

## Slide 115: Pile-up Suppression in ATLAS
past bunch crossings
following bunch crossings

## Slide 116: Pile-up Suppression in ATLAS
past bunch crossings
following bunch crossings

## Slide 117: Pile-up Suppression in ATLAS
past bunch crossings
following bunch crossings

## Slide 118: Pile-up Suppression in ATLAS
past bunch crossings
following bunch crossings

## Slide 119: Pile-up Suppression in ATLAS
past bunch crossings
following bunch crossings

## Slide 120: Pile-up Suppression in ATLAS
decreasing pile-up history
increasing pile-up effect on signal

## Slide 121: Pile-up Suppression in ATLAS
Online pile-up suppression
  Attempt to compensate signal contributions from in-time pile-up by suppression from physics signals in the pile-up history
    Can only suppress average in-time pile-up contribution in any given calorimeter cell
  Residual in-time pile-up effects still to be addressed offline
    Non-gaussian fluctuations in signal from minimum bias events in a given cell – tails due to physics fluctuations and coherent noise effects
  Distortion of pile-up history
    LHC bunch structure and super-structure makes pile-up history dependent on phase with respect to bunch gaps
Works better in high lumi/high bunch crossing scenario
  Better cancellation with more stable average energy & finer integration of pulse shape
Chart: 

## Slide 122: Pile-up Suppression in ATLAS
Online pile-up suppression
  Attempt to compensate signal contributions from in-time pile-up by suppression from physics signals in the pile-up history
    Can only suppress average in-time pile-up contribution in any given calorimeter cell
  Residual in-time pile-up effects still to be addressed offline
    Non-gaussian fluctuations in signal from minimum bias events in a given cell – tails due to physics fluctuations and coherent noise effects
  Distortion of pile-up history
    LHC bunch structure and super-structure makes pile-up history dependent on phase with respect to bunch gaps
Works better in high lumi/high bunch crossing scenario
  Better cancellation with more stable average energy & finer integration of pulse shape
in-time + next
over-compensation due to lack of next bunch-crossing w/collisions

## Slide 123: Pile-up Suppression in ATLAS
Online pile-up suppression
  Attempt to compensate signal contributions from in-time pile-up by suppression from physics signals in the pile-up history
    Can only suppress average in-time pile-up contribution in any given calorimeter cell
  Residual in-time pile-up effects still to be addressed offline
    Non-gaussian fluctuations in signal from minimum bias events in a given cell – tails due to physics fluctuations and coherent noise effects
  Distortion of pile-up history
    LHC bunch structure and super-structure makes pile-up history dependent on phase with respect to bunch gaps
Works better in high lumi/high bunch crossing scenario
  Better cancellation with more stable average energy & finer integration of pulse shape
in-time only

## Slide 124: Pile-up Suppression in ATLAS
Online pile-up suppression
  Attempt to compensate signal contributions from in-time pile-up by suppression from physics signals in the pile-up history
    Can only suppress average in-time pile-up contribution in any given calorimeter cell
  Residual in-time pile-up effects still to be addressed offline
    Non-gaussian fluctuations in signal from minimum bias events in a given cell – tails due to physics fluctuations and coherent noise effects
  Distortion of pile-up history
    LHC bunch structure and super-structure makes pile-up history dependent on phase with respect to bunch gaps
Works better in high lumi/high bunch crossing scenario
  Better cancellation with more stable average energy & finer integration of pulse shape
in-time only

## Slide 125: Pile-up Suppression in ATLAS
Online pile-up suppression
  Attempt to compensate signal contributions from in-time pile-up by suppression from physics signals in the pile-up history
    Can only suppress average in-time pile-up contribution in any given calorimeter cell
  Residual in-time pile-up effects still to be addressed offline
    Non-gaussian fluctuations in signal from minimum bias events in a given cell – tails due to physics fluctuations and coherent noise effects
  Distortion of pile-up history
    LHC bunch structure and super-structure makes pile-up history dependent on phase with respect to bunch gaps
Works better in high lumi/high bunch crossing scenario
  Better cancellation with more stable average energy & finer integration of pulse shape
in-time only

## Slide 126: Effects of Pile-up in ATLAS
More observations for 2011 ATLAS data
  Effective pile-up suppression
    Depends on distance from front of bunch train
    Depends on distance to back of bunch train
    Depends on gaps between bunch trains
      9, 20, 25, >> 25 bX…
  Digital filtering effect
    Fitting fixed physics pulse shape puts signal (“energy”) in time slots without bunch crossing
      Especially observed in last bunch crossing at end of train – expected over-compensation by history from previous bunch crossings only for τbx = 25 ns, but also observed for τbx = 50 ns!
Understanding pile-up in ATLAS
  Not as simple as adding particles from additional in-time collisions
    ATLAS sees a reduced signal from those
  Overall signal contribution is complex
    Depends not only on number of additional collisions
    Need to estimate average pile-up “around” triggered event ()

## Slide 127
Calorimeter Response

## Slide 128: Calorimeter Response
What does signal or energy scale mean?
  Indicates a certain level of signal reconstruction
    Standard reconstruction often stops with a basic signal scale
  Electromagnetic energy scale is a good reference
    Uses direct signal proportionality to electron/photon energy
    Accessible in test beam experiments
    Can be validated with isolated particles in collision environment
    Provides good platform for data and simulation comparisons
    Does not necessarily convert the electron signal to the true photon/electron energy!
  Hadronic signals can also be calculated on this scale
    Good platform for comparisons to simulations
    But does not return a good estimate for the deposited energy in non-compensating calorimeters – see later discussion!
  Is not a fundamental concept of physics!
    Is a calorimeter feature
    Definition varies from experiment to experiment

## Slide 129: Hadronic Response (1)
D.Groom et al., NIM A338, 336-347 (1994)

## Slide 130: Hadronic Response (2)
Observable
provides experimental access to characteristic calorimeter variables in pion test beams by fitting h/e, Ebase and m from the energy dependence of the pion signal on electromagnetic energy scale:
Note that e/h is often constant, for example: in both H1 and ATLAS about 50% of the energy in the hadronic branch generates a signal, with this fraction being independent of the energy itself

## Slide 131: Jet Response
Complex mixture of hadrons and photons
  Not a single particle response
  Carries initial electromagnetic energy
    Mainly photons
Very simple response model
  Assume the hadronic jet content is represented by 1 particle only
    Not realistic, but helpful to understand basic response features
More evolved model
  Use fragmentation function in jet response
    This has some practical considerations
      E.g. jet calibration in CDF
  Gets non-compensation effect
    Does not address acceptance effect due to shower overlaps

## Slide 132: Jet Response
Complex mixture of hadrons and photons
  Not a single particle response
  Carries initial electromagnetic energy
    Mainly photons
Very simple response model
  Assume the hadronic jet content is represented by 1 particle only
    Not realistic, but helpful to understand basic response features
More evolved model
  Use fragmentation function in jet response
    This has some practical considerations
      E.g. jet calibration in CDF
  Gets non-compensation effect
    Does not address acceptance effect due to shower overlaps

## Slide 133: Jet Response
Complex mixture of hadrons and photons
  Not a single particle response
  Carries initial electromagnetic energy
    Mainly photons
Very simple response model
  Assume the hadronic jet content is represented by 1 particle only
    Not realistic, but helpful to understand basic response features
More evolved model
  Use fragmentation function in jet response
    This has some practical considerations
      E.g. jet calibration in CDF
  Gets non-compensation effect
    Does not address acceptance effect due to shower overlaps
Energy (GeV)
Response Ratio

## Slide 134: Jet Response
Complex mixture of hadrons and photons
  Not a single particle response
  Carries initial electromagnetic energy
    Mainly photons
Very simple response model
  Assume the hadronic jet content is represented by 1 particle only
    Not realistic, but helpful to understand basic response features
More evolved model
  Use fragmentation function in jet response
    This has some practical considerations
      E.g. jet calibration in CDF
  Gets non-compensation effect
    Does not address acceptance effect due to shower overlaps

## Slide 135
ATLAS Detector

## Slide 136: ATLAS – Multipurpose LHC Detector
Total weight : 7000 t
Overall length: 46 m
Overall diameter: 23 m
Magnetic field: 2T solenoid
+ toroid

## Slide 137: Detector Systems in Multi-purpose Collider Experiments (1)
Tracking (inner detector)
  Closest to the interaction vertex
  Reconstructs charged particle tracks in magnetic field
    Charged particles generate current Silicon pixel elements → fit tracks to (x,y,z) space points defined by hit sensor location
    Collect secondary charges from gas ionizations by passing charged particles on wires in electric fields → fit tracks to space point in (x,y) plane and z from pulse timing
    Solenoid field allows very precise pT reconstruction and less precise p reconstruction
  Reconstructs interaction vertices
    Vertex reconstructed from track fits
    More than one vertex possible
      B-decays
      Multiple proton interaction (pile-up)
    Primary vertex defined by or
  Advantages and limitations
    Very precise for low pT measurements
    Only sensitive to charged particles
    Limited polar angle coverage
      Forward region in experiment excluded

## Slide 138: Detector Systems in Multi-purpose Collider Experiments (1)
Tracking (inner detector)
  Closest to the interaction vertex
  Reconstructs charged particle tracks in magnetic field
    Charged particles generate current Silicon pixel elements → fit tracks to (x,y,z) space points defined by hit sensor location
    Collect secondary charges from gas ionizations by passing charged particles on wires in electric fields → fit tracks to space point in (x,y) plane and z from pulse timing
    Solenoid field allows very precise pT reconstruction and less precise p reconstruction
  Reconstructs interaction vertices
    Vertex reconstructed from track fits
    More than one vertex possible
      B-decays
      Multiple proton interaction (pile-up)
    Primary vertex defined by or
  Advantages and limitations
    Very precise for low pT measurements
    Only sensitive to charged particles
    Limited polar angle coverage
      Forward region in experiment excluded

## Slide 139: ATLAS Tracking
Inner detector |η|<2.5
  Silicon Pixels
    High precision tracker
    3 cylindrical layers central
    2 x 3 disks end-cap
  Silicon Microstrip Tracker (SCT)
    High precision tracker
    4 cylindrical layers central
    2 x 9 disks end-cap
  Transition Radiation Tracker (TRT)
    Large radius tracking
    73 straw planes central
    160 straw planes end-cap
JINST 3:S08003,2008
ATLAS-CONF-2011-012
ATLAS-CONF-2010-058

## Slide 140: Detector Systems in Multi-purpose Collider Experiments (2)
Calorimeters
  Usually wrapped around inner detector
  Measure the energy of charged and neutral particles
    Uses the energy deposited by particles to generate signal
    Collects light or electric charges/current from this energy deposit in relatively small volumes
    Only works if particle energy can be fully absorbed
  Signals are space points with energy
    Reconstructs direction and energy from known position of energy deposit
    Needs assumption for “mass” to convert signal to full four momentum
      ATLAS: m = 0
  Advantages and limitations
    Gains relative energy resolution power with increasing particle energy
    Gives good energy measure for all particles except muons and neutrinos
      Muons not fully absorbed!
    Large coverage around interaction region
      “4 π” detector – except for holes for beam pipes
    Relation of incoming (deposited) energy and signal is particle type dependent
      Also need to absorb all energy – large detector system
    Does not work well for low energies
      Particles have to reach calorimeter
      Noise in readout
    Slow signal formation in LHC environment

## Slide 141: Detector Systems in Multi-purpose Collider Experiments (2)
Calorimeters
  Usually wrapped around inner detector
  Measures the energy of charged and neutral particles
    Uses the energy deposited by particles to generate signal
    Collects light or electric charges/current from this energy deposit in relatively small volumes
    Only works if particle energy can be fully absorbed
  Signals are space points with energy
    Reconstructs direction and energy from known position of energy deposit
    Needs assumption for “mass” to convert signal to full four momentum
      ATLAS: m = 0
  Advantages and limitations
    Gets more precise with increasing particle energy
    Gives good energy measure for all particles except muons and neutrinos
      Muons not fully absorbed!
    Large coverage around interaction region
      “4 π” detector – except for holes for beam pipes
    Relation of incoming (deposited) energy and signal is particle type dependent
      Also need to absorb all energy – large detector system
    Does not work well for low energies
      Particles have to reach calorimeter
      Noise in readout
    Slow signal formation in LHC environment
Tile Calorimeters
Electromagnetic Liquid Argon
Calorimeters
Hadronic Liquid Argon EndCap Calorimeters
Forward Liquid Argon Calorimeters

## Slide 142: The ATLAS Calorimeter
Basic calorimeter setup
  Large full coverage calorimeter
  system
    |η|<4.9 pseudorapidity coverage
    No azimuthal cracks &
    discontinuities
  Mixed technologies
  matching precision
  requirements
    Electromagnetic liquid argon/lead
    calorimeters with accordion absorber
    Central hadronic iron/scintillator
    calorimeter with tiled
    sampling structure
    Hadronic liquid argon/copper with
    parallel plate absorbers
    Forward liquid argon/copper and liquid argon/tungsten calorimeter
    with tubular electrodes
Basic calorimeter readout features
  Low noise readout with fast shaping time
    High sensitivity to small energy deposits
    Pile-up suppression by bi-polar signal shaping (LAr) or fast uni-polar shaping (tile)
  Non-compensating calorimeters
    Typical e/π signal ratio is 1.3
  Highly granular detector with up to 7 longitudinal segments
    Allows measuring electromagnetic and hadronic shower shapes
    About 190,000 individual readout channels
    Allows for dynamic calibration approach for hadrons and jets

## Slide 143: ATLAS Calorimetry
Barrel EM
EndCap EM
HAD Barrel,
EndCap, Forward
JINST 3:S08003,2008
JINST 3:S08003,2008
JINST 3:S08003,2008

## Slide 144
Additional Material

## Slide 145
ATLAS Calorimeters

## Slide 146: ATLAS: A General Purpose Detector For LHC
Total weight : 7000 t
Overall length: 46 m
Overall diameter: 23 m
Magnetic field: 2T solenoid + (varying) toroid field

## Slide 147: ATLAS Calorimeters

## Slide 148: The ATLAS Calorimeters
EM Endcap EMEC
EM Barrel EMB
Hadronic Endcap
Forward
Tile Barrel
Tile Extended Barrel
Electromagnetic Barrel
  |η| < 1.4
  Liquid argon/lead
Electromagnetic EndCap
  1.375 < |η| < 3.2
  Liquid argon/lead
Hadronic Tile
  |η| < 1.7
  Scintillator/iron
Hadronic EndCap
  1.5 < |η| < 3.2
  Liquid argon/copper
Forward Calorimeter
  3.2 < |η| < 4.9
  Liquid argon/copper and liquid argon/tungsten
Varying (high) granularity
  Mostly projective or pseudo-projective readout geometries
  Nearly 200,000 readout channels in total
Overlaps and transitions
  Some complex detector geometries in crack regions

## Slide 149: Electromagnetic Calorimetry
Highly segmented lead/liquid argon accordion calorimeter
  Projective readout geometry in pseudo-rapdity and azimuth
    More than 170,000 independent readout channels
  No azimuthal discontinuities (cracks)
    Total depth > 24 X0 (increases with pseudo-rapidity)
  Three depth segments
    + pre-sampler (limited coverage, only η < 1.8)
Strip cells in 1st layer
  Thin layer for precision direction and e/π and e/γ separation
    Total depth ≈ 6 X0 (constant)
  Very high granularity in pseudo-rapidity
    Δη × Δφ ≈ 0.003 × 0.1
Deep 2nd layer
  Captures electromagnetic shower maximum
    Total depth ≈ 16-18 X0
  High granularity in both directions
    Δη × Δφ ≈ 0.025 × 0.025
Shallow cells in 3rd layer
  Catches electromagnetic shower tails
    Electron and photon identification
    Total depth ≈ 2-12 X0 (from center to outer edge in pseudo-rapidity)
  Relaxed granularity
    Δη × Δφ ≈ 0.05 × 0.025
Electromagnetic Barrel

## Slide 150: Hadronic Calorimetry
Central and Extended Tile calorimeter
  Iron/scintillator with tiled readout structure
  Three depth segments
Quasi-projective readout cells
  Granularity first two layers
    Δη × Δφ ≈ 0.1 × 0.1
  Third layer
    Δη × Δφ ≈ 0.2 × 0.1
Very fast light collection
  ~50 ns reduces effect of pile-up to ~3 bunch crossings
  Dual fiber readout for each channel
    Two signals from each cell

## Slide 151: EndCap Calorimeters
Electromagnetic “Spanish Fan” accordion
  Highly segmented with up to three longitudinal segments
  Complex accordion design of lead absorbers and electrodes
    Looks like an unfolded spanish fan
Hadronic liquid argon/copper calorimeter
  Parallel plate design
  Four longitudinal segments
  Quasi-projective cells
Hadronic
EndCap
wedge

## Slide 152: Forward Calorimeters
FCal1
FCal2
FCal3
Design features
  Compact absorbers
    Small showers
  Tubular thin gap electrodes
    Suppress positive charge build-up (Ar+) in high ionization rate environment
    Stable calibration
  Rectangular non-projective readout cells
Electromagnetic FCal1
  Liquid argon/copper
    Gap ~260 μm
Hadronic FCal2
  Liquid argon/tungsten
    Gap ~375 μm
Hadronic FCal3
  Liquid argon/tungsten
    Gap ~500 μm
Forward calorimeter electrode
Readout pattern
Readout sums (detail)

## Slide 153: ATLAS Calorimeter Summary
Non-compensating calorimeters
  Electrons generate larger signal than pions depositing the same energy
    Typically e/π ≈ 1.3
High particle stopping
power over whole
detector acceptance |η|<4.9
  ~26-35 X0 electromagnetic
  calorimetry
  ~ 10 λ total for hadrons
Hermetic coverage
  No significant cracks in
  azimuth
  Non-pointing transition between barrel, endcap and forward
    Small performance penalty for hadrons/jets
High granularity
  Nearly 200,000 readout channels
    Highly efficient particle identification
    Jet substructure resolution capabilities
    Local hadronic calibration using signal shapes
    …

## Slide 154
Digital Calorimeter
Signal Filtering
in ATLAS

## Slide 155: ATLAS Digital Filtering
What is digital filtering
  Unfolds the expected (theoretical) pulse shape from a measured pulse shape
Determines signal amplitude and timing
  Minimizes noise contributions
    Noise reduced by ~1.4 compared to single reading
    Note: noise depends on the luminosity
  Requires explicit knowledge of pulse shape
    Folds triangular pulse with transmission line characteristics and active electronic signal shaping
    Characterized by signal transfer functions depending on R, L, C of readout electronics, transmission lines
Filter coefficients from calibration system
  Pulse “ramps” for response
    Inject known currents into electronic chain
    Use output signal to constrain coefficients
  Noise for auto-correlation
    Signal history couples fluctuations in time sampled readings
W.E. Cleland and E.G. Stern, Nucl. Inst. Meth. A338 (1994) 467.

## Slide 156: ATLAS Digital Filtering
What is digital filtering
  Unfolds the expected (theoretical) pulse shape from a measured pulse shape
Determines signal amplitude and timing
  Minimizes noise contributions
    Noise reduced by ~1.4 compared to single reading
    Note: noise depends on the luminosity
  Requires explicit knowledge of pulse shape
    Folds triangular pulse with transmission line characteristics and active electronic signal shaping
    Characterized by signal transfer functions depending on R, L, C of readout electronics, transmission lines
Filter coefficients from calibration system
  Pulse “ramps” for response
    Inject known currents into electronic chain
    Use output signal to constrain coefficients
  Noise for auto-correlation
    Signal history couples fluctuations in time sampled readings
W.E. Cleland and E.G. Stern, Nucl. Inst. Meth. A338 (1994) 467.

## Slide 157: ATLAS Digital Filter Coefficients

## Slide 158
Calorimeter Signal
In The Presence Of
Noise

## Slide 159: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Small signal:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression

## Slide 160: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Small signal:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression

## Slide 161: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Small signal:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression

## Slide 162: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Small signal:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression

## Slide 163: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Large signal:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression

## Slide 164: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Large signal:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression

## Slide 165: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Large signal:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression

## Slide 166: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Large signal:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression

## Slide 167: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Large signal:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression
calorimeter response < true signal!

## Slide 168: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Small signal, two particles:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression

## Slide 169: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Small signal, first particle:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression

## Slide 170: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Small signal, first and second particle:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression

## Slide 171: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Small signal, two particle, sum:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression

## Slide 172: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Small signal, two particles:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression

## Slide 173: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Small signal, two particles:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression

## Slide 174: Acceptance and Noise in Jet Response
Noise
  Fluctuations of the “zero” or “empty” signal reading
    Pedestal fluctuations
  Independent of the signal from particles
    At least to first order
  Mostly incoherent
    No noise correlations between readout channels
      Noise in each channel is independent oscillator
  Gaussian in nature
    Pedestal fluctuations ideally follow normal distribution around 0
    Width of distribution (1 σ) is noise value
Signal significance
  Noise can fake particle signals
    Only signals exceeding noise can be reliably measured
  Signals larger than 3 × noise are very likely from particles
    Gaussian interpretation of pedestal fluctuations
  Calorimeter signal reconstruction aims to suppress noise
    Average contribution = 0, but adds to fluctuations!
Small signal, two particles:
  Noise only
  Signal on top of noise
  Sum of noise and signal
  Signal after noise suppression
calorimeter response < true signal!